## Slide 1: Providing the E in G x E x M (well, most of the E)
daryl herzmann
@akrherz
Agronomy 600B
5 Feb 2020

## Slide 2: Genetics (G) x Environment (E) x Management (M)
Dr Jerry Hatfield’s et al review paper (Agronomy Journal 2015) introduces M into the G x E equation to increase actual yield vs just yield potential.
Knowledge of the Environment and Genetics can inform Management decisions.
Environmental variables relevant to G x E x M, our topics for today
  Air Temperature, Humidity, and Wind
  Precipitation
  Solar Radiation
  Soil Moisture and Temperature

## Slide 3: Providing (most of) the E Iowa Environmental Mesonet
https://mesonet.agron.iastate.edu (Google: “IEM ISU”)
ISU Agronomy project since 2001
“Mesonet” is a meteorology term describing a network of observations on a spatial scale ~10s km
Crazy website with all kinds of apps and portals to get lost in and cry over.
Please please please, the main point for today, if you have trouble:
Tweet me! @akrherz
Call me! 515 294 5978
Stop by my office! 3027 Agronomy
Email me! akrherz@iastate.edu

## Slide 4
The website aggregates data from many different data sources.
Data is generally organized by acronym heavy “Networks”,
  ISU Soil Moisture Network is one such network.
“Daily Feature” highlights some relevant and deep linked plot each day.

## Slide 5: IEM Aggregated Networks
Acronym / Title | Description
ASOS / AWOS | General classification of Airport weather stations operated by the FAA, NWS, DoD, and state DOTs.
CoCoRaHS | Citizen science reporting “daily” snowfall, snow depth and precipitation.
NWS COOP | National Weather Service Cooperative Observers reporting “daily” high and low temperatures, precipitation, and snowfall.
DCP | General grouping of many different types of sensors that focus on hydrology.
ISU Soil Moisture | Iowa State operated network of weather stations focused on Agriculture weather data needs.
NLAE Flux | Advanced monitoring stations by the USDA NLAE monitoring various fluxes from agricultural landscapes.
RWIS | DOT Roadway Weather Information Systems monitoring weather and pavement state.
SCAN | USDA Soil Climate Analysis Network
Other | Various other stations.

## Slide 6: Which network should I use?
Data Need | Time Interval | Recommendation
“Daily” High/Low Temps + Precipitation | Daily | NWS COOP IEM “Long Term Climate” / “Climodat”
Air Temperatures + Precipitation (not snow) | Hourly | ASOS/AWOS + ISU Soil Moisture
Wind | Daily + Hourly | ISU Soil Moisture ASOS / AWOS (Airport weather stations)
Solar Radiation | Daily + Hourly | ISU Soil Moisture
Soil Temperature/Moisture | Daily + Hourly | ISU Soil Moisture / SCAN
Humidity | Daily + Hourly | ISU Soil Moisture / ASOS / AWOS

## Slide 7
Select Plot Type
Select Plot Options
Description
Custom Generated Plot
Download Raw Data (Excel)
IEM Auto Plotting

## Slide 8: ISU Soil Moisture Station
Wind Speed
+ Direction
Solar Panel
Solar Radiation
Air Temp + Humidity
Logger Enclosure
Bare soil for 4 inch
Depth Soil Temperature
Tipping Bucket
Rain Gauge
12, 24, & 50 inch depth
Soil Temperature + Moisture

## Slide 9: Data Variables to Discuss
Air Temperature, Humidity, and Wind
Precipitation
Soil Moisture/Temperature
Solar Radiation

## Slide 10: Understanding micro-climates
Subtle topography / elevation change makes a difference!
We don’t have enough sensors nor sensor sensitivity to measure this effect.
If you are studying agronomic variability at this scale, you likely need to consider that weather/climate varies too.
Photo: Dr Elywnn Taylor

## Slide 11: Urban Heat Island
Urban areas are generally warmer than rural due to albedo and heat holding capacity differences.
UHI is even noticeable in smaller Iowa towns.
Magnitude of this difference may not matter for your usage case.
Web Link

## Slide 12: Soil Differences
Web Link
Waterloo’s site has soil with larger sand content and will cool faster under light wind condition.

## Slide 13: Relative Humidity
As the name implies, the value is relative.
On average, the lowest RH values happen in the spring/fall (black line).
Daily average RH is about the same in summer and winter (huh?)
Web Link

## Slide 14: Vapor Pressure Deficit (VPD)
VPD is a more direct and comparable measure of humidity.
Air’s demand / pull of water vapor.
2019 values show a decreased demand from average.
Web Link

## Slide 15
ISU “Tall Towers” 1 second interval Wind Speed [mps]
Two sensors at same height, mounted at different directions on the tower. We also have 20 Hz data 
This entire plot is just 1 minute of data!

## Slide 16
Web Link
February
August

## Slide 17: Data Variables to Discuss
Air Temperature, Humidity, and Wind
Precipitation
Soil Moisture/Temperature
Solar Radiation

## Slide 18: Precipitation Variability
Iowa Flood Center experiment with tipping buckets 3 feet apart
Found some cases of noticeable differences between these two gauges
In general case, which gauge is right? 
http://iowafloodcenter.org/notes-from-the-field-rain-gauges/

## Slide 19: Bah, My weather station at my house is highly accurate!
https://www.wunderground.com/weatherstation/installationguide.asp

## Slide 20: The answer to: “How much did it rain in Ames on 25 June 2010?”
IEM QC COOP | 0.00 | SchoolNet | 0.57 | CoCoRaHS | ??? | Stage IV | 0.22
ASOS | 0.13 | RWIS | 0 ? | ISUAG AgFm | 0.25 | NARR | 0.19
ASOS DSM | 1.11 | Lincoln Way | 0 ? | Others | 0.53 | TRMM | 0.51
ASOS DSM Hr | 0.33 | Ada Hayden | 0.93 | DMX 1hr | 0.30 |  | 
ASOS 1min | 0.36 | H2O Trtment | 0.47 | DMX Storm T | 0.25 |  | 
We simply average and get: 0.36176470588 inches! What precision!

## Slide 21: Data Variables to Discuss
Air Temperature, Humidity, and Wind
Precipitation
Soil Moisture/Temperature
Solar Radiation

## Slide 22: ISU Soil Moisture Caveats Galore
Only 12, 24, and 50 inch depth readings for moisture + temperature
4 inch soil temperature is not in the crop field
Sensors don’t work properly when soil is frozen
We’ve had issues with lightning knocking out sensors
Newly installed sensors need time to find equilibrium

## Slide 23
Web Link

## Slide 24
Web Link (Autoplot #177)

## Slide 25
Web Link

## Slide 26: Data Variables to Discuss
Air Temperature, Humidity, and Wind
Precipitation
Soil Moisture/Temperature
Solar Radiation

## Slide 27: Clear vs Party Cloudy
One minute resolution data shows the impact of individual clouds.
Do you need to know this variability?
Web Link

## Slide 28
Web Link
Gold Star for whomever knows what this is?
More radiation than during a clear day?

## Slide 29: Corn Grain Dry Down Tool

## Slide 32: OK, enough of my rambling…. Questions? https://mesonet.agron.iastate.edu “Info” Tab -> Presentations
Twitter: @akrherz
akrherz@iastate.edu
515-451-9249